## Slide 1: Final project
Team
Tsourdinis Theodoros
Chatzistefanidis Ilias
WiFi Spectrum Analyzer

## Slide 2: Project’s purpose
Computing WiFi Channel’s Traffic
Finding Optimal Channel
Extracting Pattern from Channel’s Occupation
Predicting Future Behavior

## Slide 3: GNU radio flowchart

## Slide 4: Measurement Technique
WiFi 2.4 GHz Spectrum
Our Technique
2.4GHz Band: 22MHz Channels with Overlapping
Measurements for 12 out of 22 MHz
measurements with 4 MHz bandwidth
for center frequencies that have distance 5 MHz from each other
Finally:
13 Measurements
11 Channels

## Slide 5: Transmission indicator
Energy Values are floats with range [-60 , +20] dB
Threshold = - 20dB
Busy_Percentage =
(# values > -20 )/( # all_values)
Busy Percentage = 3%
Busy Percentage = 30%
dB
dB

## Slide 6: OUR ALGORITHM – PYTHON scripts
For T iterations:
spectrum measurements  binary files
convertion to decimal
calculation of Busy_Percentage
  create 3 real-time plots:
  i) Current Plot
  ii) Average Plot
  iii) Time plot
  Busy_Percentage  output.txt

## Slide 7
RESULTS – 2.5 Hours

## Slide 8
Time Series Forecasting
Long short-term memory (LSTM) Recurrent Neural Networks.
Split Data to :
        First 2.0 hours (80 iterations) for Training
        Last 0.5 hours (20 iterations) for Testing
Prepare Data for model ( 3D Input )
FUTURE FORECASTING

## Slide 9: PREDICTIONS
Predicted Busy_Percentage = 6.98 %
Real Busy_Percentage = 5.63 %
Optimal - Channel 9

## Slide 10: PREDICTIONS

## Slide 11: PREDICTIONS
Predicted Optimal : Channel 9
Measured Optimal : Channel 9
For last 0.5 / 2.5 hours:

## Slide 12: THANK YOU FOR YOUR ATTENTION!